## Slide 1: SMART HOME AUTOMATION SYSTEM
PRESENTED BY- VANSH SHARMA
cs(iot)

## Slide 2: OBJECTIVE
To develop a smart home automation system using Arduino.
Automate tasks such as:
Lighting control using LDR sensor.
Intrusion detection with PIR motion sensor.
Gas leak detection using MQ-2 sensor.
Smart door control with ultra sonic sensor and servo motor.
Display real time status and alerts on a LCD screen. Enhance safety,convenience ,and energy efficiency in the home environment.

## Slide 3: COMPONENTS USED
Arduino UNO
LCD 16x2 Display
LDR Sensor
Gas Sensor (MQ-2)
PIR Motion Sensor
Ultrasonic Sensor
Servo motor
Buzzer
Relay module
Bread Board and wires
Power Supply
Slide Switch
Resistor
Bulb
Dc Motor

## Slide 5: CIRCUIT DIAGRAM

## Slide 6: CODE

## Slide 7: ARDUINO CODE OVERVIEW
LDR controls a relay to switch a bulb based on light intensity
PIR sensor detects motion and controls dc motor
GAS sensor detects LPG leakage and activates a buzzer
Ultrasonic sensor detects presence at door and activates servo
LCD displays sensor readings and system messages

## Slide 8: LDR AND RELAY CONTROL
LDR Monitors ambient light
If light intensity <600, bulb turns OFF.
If >600, darkness bulb turns ON
LCD displays current light value and status

## Slide 9: If light intensity>600, bulb turns ON

## Slide 10: If light intensity<600, bulb turns OFF

## Slide 11: PIR MOTION DETECTION
PIR sensor detects human movement
If motion detected: MOTOR ROTATES, BULB TURNS ON
If no motion detected: MOTOR STOPS, BULB TURNS OFF

## Slide 12: WHEN MOTION DETECTED : MOTOR ROTATES, BULB TURNS ON

## Slide 13: GAS DETECTION AND ALARM
MQ-2 gas sensor detects gas concentration.
If value <=85 LCD display LOW
If value <=120 LCD display MED
If value <=200 LCD display HIGH
If value <=300 LCD display EXT
If value above 300 then buzzer turns ON

## Slide 14: If value <=85 LCD display LOW

## Slide 15: If value <=120 LCD display MED

## Slide 16: If value <=200 LCD display HIGH

## Slide 17: If value <=300 LCD display EXT

## Slide 18: If value above 300 then buzzer turns ON

## Slide 19: ULTRASONIC+SERVO FOR SMART DOOR
Ultrasonic Sensor measures distance.
If distance < 40 cm Servo rotates 90 DEGREE
LCD displays DOOR OPEN
If distance > 40 cm Servo = 0 DEGREE
LCD displays DOOR OFF

## Slide 20: If distance < 40 cm Door OPENS

## Slide 21: If distance > 40 cm Door closes

## Slide 22: CONCLUSION
Integrates various sensors and modules into a smart home model.
Helps automate lighting, security, gas leakage alert, and door control.
Ideal for low-cost ,Arduino-based home automation projects.

## Slide 23: THANK YOU